## Slide 1: Mobile Application for Intelligent Transportation Systems with Vehicular Communications Integration
A multi-platform mobile application designed to interface with either vehicles or a central information broker, facilitating monitoring and interaction within the ITS environment. The application integrates sensor data collection and sharing, enabling users to create and visualize events that warn of potential hazards such as accidents, traffic jams, road works, and adverse weather conditions in real-time, thereby helping to prevent accidents and reduce congestion.
Gil Teixeira – gilteixeira@ua.pt
José Fonseca – jaf@ua.pt, João Almeida – jmpa@ua.pt
Joaquim Ferreira – jjcf@ua.pt

## Slide 2: Motivation

## Slide 3: C-ITS (Cooperative Intelligent Trabsoirtation Systems)
C-ITS architecture
A subset of ITS focused on vehicular communications
Direct communications
  Contextually relevant informations
  Significantly reduced delay
Vechile-To-Everything (V2X) services
  Tolling
  Electric Vehicle (EV) charging

## Slide 4: Application Architecture
Mobile application architecture and external connections
React Native (RN)
  Javascript / Typescript
  Expo
Sensor Data Collection
Message Queuing Telemetry Transport (MQTT)

## Slide 5: User Modes
Vulnerable Road User (VRU)
  Quadtrees - Geographicly relevant information filter
  VRU Awareness Messages (VAMs)
Traffic Control Center (TCC)
  Monitoring
On-Board Unit (OBU)
  Contextually relevant information
  Vehicle-To-Everything (V2X) Services
User mode toggle switch

## Slide 6: European Telecommunications Standards Institute (ESTI) Messages
CPM - Collective Perception Message​
CAM - Cooperative Awareness Message​
IVIM - Infrastructure to Vehicle Information Message​
HDMAP - ​High-Definition Maps
CPM and CAMs
HDMAP
IVIM

## Slide 7: ESTI Messages
DENM - Decentralized Environmental Notification Message
VAM - VRU Awareness Message
DENM creation

## Slide 8: ESTI Messages
SAEM – Services Announcement Essential Message
EVCSNM – Electric Vehicle Charging Spot Notification Message
EVRSRM – Electric Vehicle Recharging Spot Reservation Message
DENM creation

## Slide 9: Proprietary Messages
CPM - Collective Perception Message​

## Slide 10: Proprietary Messages
CPM - Collective Perception Message​