## Slide 1
A Mobile App for Intelligent Transport Systems with Vehicle Communications Integration. A monitoring system for the road infrastructure equipped with ITS technology, capable of identifying risky driving conditions.
Gil Teixeira – gilteixeira@ua.pt
José Fonseca – jaf@ua.pt
João Almeida – jmpa@ua.pt, Joaquim Ferreira – jjcf@ua.pt

## Slide 2: Motivation
Increasingly high number of vehicles
  Road degradation
  Congestion
  Accidents
Climate change
  Dangerous weather events
VRUs are the most endangered!
  C-ITS and V2X
  Cooperative Awareness
Vehicles in use in Europe

## Slide 3: Objectives / User Modes
Objectives:
Warn road users
  Weather events
  Road events
Directly involve VRUs
  Location sharing
  Report of events
Traffic Control Centre monitoring
Vehicular communications
  Sensors sharing
  Tolling
  EV charging
User Modes:
VRU mode (left)
TCC mode (centre)
OBU mode (right)
User mode switch

## Slide 4: Message Queuing Telemetry Transport
All information is exchanged using an MQTT broker.
Lightweight protocol with a publish/subscribe model.
Topic structure and quadtree allows for a user to subscribe only to it’s nearby messages!

## Slide 5: Mobile App Development
Multi-platform:
Android (72.37%)
iOS (26.98%)
Single code base (Typescript and Javascript only!):
React Native
Expo
Stateless message storage with periodic refresh for stable performance.

## Slide 6: Cooperative, Connected and Automated Mobility Messages
CPM
  Cooperative Perception Message
CAM
  Cooperative Awareness Message
IVIM
  I2V Information Message
IVIM
CPMs and CAMs

## Slide 7: CCAM Messages
VAM
  VRU Awareness Message
DENM
  Decentralized Environmental Notification Message
VAMs
DENMs
Menu

## Slide 8: A-To-Be Messages
HEARTBEAT
SAEM
  Service Announcement Essential Message
TPM
  Tolling Payment Message
HDMAP
  High Definition Map
HDMAP
SAEM and TPM
HEARTBEAT

## Slide 9: Sensor Messages
VSM
  Vehicular Sensor Message
  SPVSM
    SmartPhone VSM
    Expo-Sensors
  OVSM
    OBD-II VSM
  SNVSM
    SoNar VSM
Phone
Sensors
Vehicle
Sensors

## Slide 10: Future Work